## Slide 1
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 01
What this simulator is
A virtual MCT photoconductor test and measurement bench for learning how controls map to observable outputs.
ORIENTATION
STUDENT ACTION
KEY TAKEAWAY
• Instrument-centered environment: Spectrum Analyzer, Oscilloscope, and I-V Characteristics. • Bench controls mirror real setup decisions: bias, temperature, BB cover, chopper, grounding, and preamp. • The session is about measurement interpretation: control -> measurement -> interpretation. • This is not the rigorous FEniCS model. It is a webinar-grade training tool built around bench behavior.
Open the simulator and identify the sidebar controls, instrument tabs, and telemetry readouts.
Treat the utility like a virtual test bench. Every slide should connect a user action to a measurable consequence.
Detector
Bias and temperature set the operating point.
Optical
BB cover and chopper define the signal injection.
Readout
Grounding, preamp, scope, and spectrum determine what you actually see.

## Slide 2
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 02
Dark resistance is the first extraction
Begin with the most familiar quantity: the covered detector current under bias.
BASELINE
STUDENT ACTION
KEY TAKEAWAY
• Cover the detector so the optical contribution is removed and only the dark electrical state remains. • Choose a bias point, read voltage and current, and compute dark resistance from the bench quantities. • This is the correct first-pass extraction because it does not rely on hidden simulator constants. • The output is immediately interpretable as a device-plus-setup electrical operating point.
Set BB cover closed. Measure V and I at one bias point and calculate R_dark.
Start from what is directly measurable. The first lesson is not hidden physics - it is disciplined extraction from bench observables.
R_dark = V / I

## Slide 3
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 03
Ohmic region versus nonlinearity
Repeat the dark-resistance calculation across low bias and ask whether the detector is approximately ohmic.
LOW-BIAS CHECK
STUDENT ACTION
KEY TAKEAWAY
• Use the same covered-detector procedure at several bias points rather than trusting a single number. • If R_dark stays nearly constant, the device is approximately ohmic in that operating region. • If R_dark drifts strongly with bias, nonlinearity or measurement-chain effects are becoming important. • For the webinar toy model, the updated low-bias trend is intentionally mild and more bench-like.
Bias | R_dark | Interpretation
0.5 V | 24.7 Ω | approx. ohmic
1.0 V | 25.0 Ω | approx. ohmic
1.5 V | 25.5 Ω | mild curvature
R_dark = V / I
Compute R_dark at 0.5, 1.0, and 1.5 V and compare the spread.
A resistance value is also a linearity diagnostic. The right question is not only “what is R?” but “does R stay stable with bias?”

## Slide 4
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 04
Temperature changes dark behavior
Detector electrical behavior is not fixed - it changes with operating temperature.
TEMPERATURE
STUDENT ACTION
KEY TAKEAWAY
• Repeat the covered-detector check at room temperature and at 77 K. • Dark resistance and the noise floor both depend on temperature, so operating point is temperature specific. • Colder operation typically shifts the detector into a cleaner electrical state and lowers Johnson-type voltage noise. • This is why cryogenic detector measurements must always be interpreted together with temperature.
Condition | Approx. R_dark
77 K | 24.6 Ω benchmark
298 K | 15.5 Ω benchmark
e_n,J = √(4 k T R)
Compare dark behavior at 298 K and 77 K before drawing any conclusions about performance.
Temperature is part of the measurement definition. A detector does not have one universal dark state independent of temperature.

## Slide 5
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 05
Opening the blackbody cover reveals photoresponse
Optical response is identified by comparing the illuminated state to the dark baseline.
ILLUMINATION
STUDENT ACTION
KEY TAKEAWAY
• The dark state provides the electrical baseline. Opening the BB cover injects the optical input. • The meaningful optical quantity is the difference between illuminated output and dark output. • In current mode, this appears as photocurrent. In voltage mode, it appears as photovoltage. • This comparison discipline prevents students from confusing static detector bias behavior with optical response.
Toggle the BB cover and compare the new electrical output against the covered-detector baseline.
Photoresponse is not interpreted in isolation. It is extracted by comparing two controlled measurement states.
I_photo = I_illuminated - I_dark

## Slide 6
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 06
Response increases with bias
With optical input held constant, normalized photovoltage or photocurrent shows how response scales with bias.
NORMALIZED RESPONSE
STUDENT ACTION
KEY TAKEAWAY
• Keep the incident optical input fixed and measure the photovoltage at several bias points. • Because the optical input is unchanged, the normalized voltage response can be compared directly from V_ph. • This lets students learn the bias trend before any hidden optical power is revealed. • The webinar uses measured output first, then absolute detector metrics later.
Bias | Photovoltage | Normalized
0.5 V | 171 µV | 1.00
1.0 V | 314 µV | 1.84
1.5 V | 419 µV | 2.45
normalized response ∝ V_ph
Measure V_ph at 0.5, 1.0, and 1.5 V and divide by the 0.5 V value.
Normalized response is enough to understand the trend. Absolute responsivity is delayed until optical input is revealed.

## Slide 7
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 07
Why chopping helps
Modulating the optical input moves the signal into a known frequency channel.
FREQUENCY DOMAIN
STUDENT ACTION
KEY TAKEAWAY
• Turn the chopper on and move from DC-style interpretation into the spectrum analyzer view. • The chopped optical input appears as a feature at the chopper frequency rather than as an ambiguous static shift. • This is the basic reason chopped measurements are easier to interpret in noisy environments. • The student begins learning that modulation is a measurement strategy, not just a convenience feature.
Go to the Spectrum Analyzer, turn the chopper on, and identify the peak at the modulation frequency.
A known modulation frequency gives the measurement a target. The student is no longer guessing where the signal should be.
Optical modulation
Detector output
Peak at f_chop

## Slide 8
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 08
Grounding separates real signal from contamination
Strong spectral features are not automatically detector physics.
BENCH HYGIENE
STUDENT ACTION
KEY TAKEAWAY
• Compare grounded and ungrounded conditions without changing the optical setup. • The chopper peak is the intentional signal. The 60 Hz and 120 Hz features are environmental contamination. • This teaches the student to identify the origin of a spectral feature before attaching physical meaning to it. • Grounding is part of the measurement, not just a background setup detail.
Toggle grounded versus ungrounded and watch which peaks move or appear.
A spectrum has to be interpreted. “Strong peak” is not enough - the student must know whether the feature comes from the detector, the modulation, or the environment.
Feature | Interpretation
f_chop peak | intentional optical signal
60 / 120 Hz | bench pickup / hum

## Slide 9
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 09
Bias changes signal quality, not just signal size
The real question is whether the useful spectral feature rises faster than the nearby floor.
SIGNAL VS FLOOR
STUDENT ACTION
KEY TAKEAWAY
• At each bias point, compare the chopper peak height to the local spectral floor near that frequency. • A larger signal is useful only if it becomes easier to distinguish from the surrounding background. • This teaches students to think in terms of detectability and measurement quality, not raw amplitude alone. • Bias choice is therefore a tradeoff, not simply “higher is always better.”
Compare the peak and nearby floor at 0.5, 1.0, and 1.5 V.
Measurement quality depends on relative contrast. Better detector operation means better signal relative to the local background, not just a bigger number.
local signal quality ~ peak / nearby floor

## Slide 10
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 10
What the preamp actually does
For the webinar toy model, the preamp is best understood as a measurement-chain conditioning stage.
PREAMP
STUDENT ACTION
KEY TAKEAWAY
• In the current toy simulator, preamp gain acts like an ideal output-side voltage gain stage. • Signal and detector-origin noise both scale with gain, so intrinsic detector SNR does not automatically improve. • The practical role of the preamp is to bring the detector output into a useful range for the next instrument: lock-in, scope, analyzer, or DAQ. • This mirrors why real test departments may always use preamps even when experimentalists remain cautious about added noise sources.
Toggle preamp gain and watch the displayed voltage scale move into a more usable instrument range.
The lesson is not “preamp makes detector better.” The lesson is “preamp helps the measurement chain use the detector output effectively.”
V_out = G · V_in

## Slide 11
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 11
Oscilloscope view: the same measurement in time
The spectrum and the scope are two views of the same detector output.
TIME DOMAIN
STUDENT ACTION
KEY TAKEAWAY
• The chopped detector response appears as structured AC behavior in time rather than as a spectral peak. • The waveform also carries noise and any contamination that the bench introduces. • The simulator reports RMS voltage, which is a compact bench quantity but not automatically pure optical signal. • The student should use the scope and spectrum together and expect them to tell a consistent measurement story.
Observe the waveform, then compare grounded versus ungrounded or low bias versus high bias.
RMS voltage is useful because it compresses a noisy waveform into one measurable number. The caution is that RMS can include both wanted and unwanted contributions.
V_rms = √[(1/N) Σ v_i²]

## Slide 12
BROOKS PHOTONICS
www.brooks-photonics.com
INTERACTIVE WEBINAR | 12
Reveal the optical input and compute absolute voltage responsivity
The payoff slide: convert normalized voltage response into a true detector metric.
RESPONSIVITY
STUDENT ACTION
KEY TAKEAWAY
• Up to now we intentionally worked with normalized response because optical input had not yet been revealed. • The toy simulator uses a hidden total incident optical power, so voltage responsivity can now be computed directly. • This makes explicit that absolute responsivity cannot be obtained from electrical output alone - optical input is also required. • The result closes the loop from bench observables to a detector performance metric.
R_v = V_ph / P_incident
Hidden toy-sim input: P_incident = 4.315 × 10^-7 W
Bias | Vph | Rv
0.5 V | 171 µV | 396 V/W
1.0 V | 314 µV | 728 V/W
1.5 V | 419 µV | 971 V/W
Use the measured photovoltage values and divide by the hidden total incident power.
Normalized response teaches trend. Revealed optical input enables absolute voltage responsivity. That is the final payoff of the session.